## Slide 1: Base64: a binary string is encoded as an ASCII string
Basic Algorithm:
  For every three bytes (24 bits) # lcm(6,8) = ?
    Load and Merge the bytes together
    Chop and Slide into 4 6-bit chunks
    Map each 6-bit chunks into a 8-bit ASCII value
    Store each new the original three bytes with four new bytes
  Add appropriate padding for remaining bytes
Mapping ensures the result 8 bits are always printable ASCII characters
Operations at the assemble level:
  byte manipulations
  shifting and masks
Working at the byte level exposes Endianness

## Slide 2: The "encode" subroutine:
The following slides illustrate the steps associated with encoding
  24-bits into 4 base64 characters
The signature (or API) of this subroutine is:
  void encode(input, output)
    input: the memory location where the three input values are stored
    output: the memory location where the four output values are to be stored
MIPS instructions to call the subroutine:
MIPS instructions to load and store the input and output within the subroutine
# Load 3 input bytes
lbu $t1, 0($a0)
lbu $t2, 1($a0)
lbu $t3, 2($a0)
# Store 4 output bytes
sb $s1, 0($a1)
sb $s2, 1($a1)
sb $s3, 2($a1)
sb $s4, 3($a1)
la $a0, input
la $a1, output
jal encode

## Slide 3: Load and Merge (shift and meld)
load:
shift:
meld:
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0
t1:
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
t2
t3:
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
0xfa
0xca
0xde
1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
t1:
 |  |  |  |  |  |  |  | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
t2:
t3:
1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
t0:
lb $t1, 0($a0)
sll $t1, $t1, 16

## Slide 4: Chop and Slide:
1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0
 |  |  |  |  |  | 1 | 1 | 1 | 1 | 1 | 1 |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 1 | 1 | 1 |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1 | 1 | 1 | 1 | 1
0xfacade
0x3F
0x3F000
0xFC0
1 | 1 | 1 | 1 | 1 | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
0xFC0000
MASKS
t0:
s3= (t0 & xFC0) >> 6 == 10 1011= 0x2B
s1= (t0 & xFC0000) >> 18= 11 1110= 0x3E
s2= (t0 & x03F000) >> 12= 10 1100= 0x2C
s4= (t0 & x03F) >> 0 == 01 1110= 0x1E
t0 &xFC0000
1 | 1 | 1 | 1 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 5: Mapping:
Base64 Mapping Table
Two approaches to mapping:
  Perform a table lookup
  Compute the value
    via the following switch statement
The computed indices are:
  s1 = 0x3E (62)
  s2 = 0x2C (44)
  s3 = 0x2B (43)
  s4 = 0x1E (30)
The mapped characters are:
  '+' (0x2B)
  's' (0x73)
  'r' (0x72)
  'e' (0x65)
switch ( index ) { 0..25 : index += 0 + 'A' ; // A - Z break; 26..51 : index += -26 + 'a'; // a - z break; 52..61 : index += -52 + '0'; // 0 - 9 break; 62 : index = '+'; break; 63 : index = '/'; break; }