## Slide 1: Languages, Compilers, and Hardware:
Source: .i
Languages
  Domain Specific
Compilers & Interpreters
  Analysis
    lexicographic
    syntactic
    semantic
  Language Optimization
  Machine Optimization
  Translation: TAC → MIPS
Hardware
  General Types: Registers / Stack
  Specific CPU Controls
CLI: compilation exercise
Languages
Hardware
Translation Process
Source: .java
Assembly: .s
Object: .o
Executable: a.out
Object: .class
Virtual Machine
javac
java
cc: ← .h, .c
.i ← cpp
.s ← ccom .o ← as
.out ← ld
Source: .c
kernel
kernel

## Slide 2: MIPS Microarchitecture

## Slide 3: MIPS Instruction Set Architecture (ISA)
General Architecture
  RISC (Reduced Instruction Set Computer)
  Simple Instructions
  Lots of Registers
  Remember Memory is SLOW!
CPU
  ALU
  32 general purpose registers
Instruction Set:
  List of Instructions Supported by the Architecture
  MIPS Cheat Sheet
Coprocessors
  Floating point
  Traps, Exceptions, Interrupts
Memory
x86: has 4 general purpose registers

## Slide 4: MIPS ISA Architecture: Registers
Data types:
  byte, half, word
  integer (signed/unsigned), binary32, binary64
Registers:
  32: 32-bit integer registers
  32: 32-bit floating point registers
    binary32: $fp0 .. $fp31
    binary64: {$fp0, $fp1} .. {$fp30, $fp31}
  3: system registers: pc, hi, lo
Integer Registers

## Slide 5: Registers
System
  PC: Program Counter
  IR: Instruction Register
  BadVAddr: memory address where exception occurred
  Status: Interrupt mask, enable bits and status when exception occurred
  Cause: Type of exception
  EPC: Address of instruction that caused the exception
Reserved (Don't use!)
  $at: reserved for the Assembler
  $k1, $k2: reserved for the Kernel
  $gp: global pointer defined by the compiler
Special (Access via specific instructions)
  PC: program counter
  hi, lo: used double word results
    (hi, lo) = val1 * val2
    (hi, lo) = val1 % val2
General Purpose
  32 32-bit integer registers: $0..$31
  32 32-bit floating point registers: $f0..$f31

## Slide 6: Category of Instructions
native instructions:
  defined by the ISA, directly corresponds to a hardware operation
idioms:
  defined by the ISA, an alternate form of a hardware instruction
  b label
    beq $zero, $zero, label
pseudo instructions:
  an alternate syntactic form of an instruction
  pseudo instruction is textual replaced with native instruction
  lb $t1, label+offset
    lui $at, &label
    lb $t1, offset($at)
macros:
  user-defined pseudo instruction
    average $v0, $t2, $t3
    average($v0, $t2, $t3)
subroutines
  user defined abstraction, resulting
    jal subroutine
    nop
  a change in control-flow
  a ownership of registers
.macro average(%d, %s, %t) addu %d, %s, %t
srl %d, 2
.end_macro
.text
subroutine: nop
jr $ra

## Slide 7: MIPS ISA Architecture: Instructions
Three basic instruction types
  Arithmetic, bitwise logic, etc.
  Data transfers
  Basic control flow
Examples:
  add $v0, $v0, $a0 # $v0 = $v0 + $a0
  addi $v0, $v0, 2 # $v0 = $v0 + 2
  srl $a0, $a1, 4 # $a0 = $a1 >>> 4
  li $t0, 4 # $t0 = 4
  move $t1, $t2 # $t1 = $t2
  lb $s0, 0($t0) # $s0 = MEM[$t0] lh $s1, 3($t0) # $s1 = concat(MEM[$t0+3+1],MEM[$t0+3+0])
  beq $t3, $t5, label # if ($t3 == $t5) goto label
  jal proc # method()
MEM
0
1
2
n-1
$t0 = 4; 0($t0) ⇔ $t0[0]
t0:
3
4

## Slide 8: MIPS ISA (Architecture) Memory Layout
Memory:
  memory layout
  byte addressable
  lowest address at bottom
  32-bit words
  little endian format
Little endian format
  recall 32-bit registers (4 bytes)
  fall to the left
4: DE
3: AD
2: BE
1: EF
1: EF
2: BE
3: AD
4: DE
1: EF
2: BE
3: AD
4: DE
$sp
$fp
$gp
endiance: the order of bytes within a word
big: 1,2,3,4 (yy/mm/dd)
little: 4,3,2,1 (dd/mm/yy)
middle: 3,4,1,2 (mm/dd/yy)

## Slide 9: Main Memory
View & Orientation
  Array of Bytes: (i.e., byte addressable)
Data Segments: (to name a few)
  .text
  .data
    .lit4, .lit8 (4 and 8 byte literals)
    .bss (block storage)
  heap
  stack
Data Declarations and Sizes
  .byte, .half, .word
  .ascii, .asciiz
  .float, .double
  .space
Alignment
Endianness
well-known addresses
current address saved in a register

## Slide 10: Memory Organization (Java program)
class Main { public static int x = 5; int y = 7; public int addNumbers(int a, int b) { int sum = a + b; return sum; } public static void main(String[] args) { int num1 = 25; int num2 = 15; // create an object of Main Main obj = new Main(); int result = obj.addNumbers(num1, num2); System.out.println("Sum is: " + result); } }
.text (INSTRUCTIONS)
.data
STACK int a; int b;
HEAP
}
}
Dynamic: Locations defined at runtime.
Static: Locations are defined when the program starts.

## Slide 11: Process Status Diagram
Control of the computer moves through a well-defined cycle
Transitions:
  admit: A request is made to allow your program to content for control
  dispatch: Your program is given control
  exit: Your program asserts that it is done
  interrupt: The OS seizes control
  trap: Your program (implicitly or explicitly) requests a service to be performed
  completion: The request is satisfied
Traps are calls to the Kernel (the OS)
admit
exit
dispatch
completion
trap
interrupt

## Slide 12: MIPS System Calls: SystemCallAPI.png
print integer
print float
print double
print string
read integer
read float
read double
read string
allocate memory
terminate
print character
read character
file open
file read
file write
file close

## Slide 14: Three Address Code (TAC)
A generic assembly language in which all instructions have at most three addresses
An address references either
  a register location
  a memory location
Immediate values are stored in a location within memory
Assumption: the assembly language is for a register-based machine, with an infinite number of registers.
Examples:
a = y + x
a = y
a = x + 2
b = d * 2 + y
  t0 = d * 2
  t1 = t0 + y
  b = t1

## Slide 15: Basic Blocks
A number of instructions in which there is
  a single entry point (via a label), and
  a single exit point (via a goto)
All programs can be broken down into a set of basic blocks
A control flow graph determines which a basic block is executed.
Standard control flow graphs
  if-then-else and all other variants (e.g., switch)
  while, do-while and all other variants
  for loop and all other variants
  call-return
label:
x = 3;
z = 5;
y = 3; goto label2
label2: