## Slide 1: Physical Architecture: MIPS Microarchitecture

## Slide 2: MIPS Architecture Overview
General Purpose Registers
  32: 32-bit integer registers: $0..$31
  32: 32-bit floating point registers: $f0..$f31
Reserved Registers (Don't use!)
  $at: reserved for the Assembler
  $gp: global pointer defined by the compiler
  $k1, $k2: reserved for the Kernel
System Registers
  BadVAddr: memory address where exception occurred
  Status: Interrupt mask, enable bits and status when exception occurred
  Cause: Type of exception
  EPC: Address of instruction that caused the exception
Special Registers (Access via specific instructions)
  PC: program counter
  hi, lo: used double word results
    (hi, lo) = val1 * val2
    (hi, lo) = val1 % val2